## Slide 1: Project Design Review
RC Plane

## Slide 2: Project Goals and Specifications
Design an RC airplane which can:
  Achieve sustained flight for 60+ seconds
  Perform turns without crashing
  Withstand mild crashes without sustaining significant damage
Stretch goals:
Land airplane successfully [belly down, no damage]
Take in-flight measurements and perform Arduino-automated tasks
  e.g. Automated turn, level flight, maintain speed, geofencing

## Slide 3: Design Choice: Structural Material
Originally wanted to 3D print the plane parts:
  Pros: Greater control over shape, easy to re-make if it breaks
  Cons: Brittle, heavy, would need to print in pieces and assemble
Instead we chose foam (model plane grade)
  Pros: Lightweight, ductile, yet rigid to wind stress. Faster to machine.
  Cons: Must buy material in bulk, more labor intensive assembly of wings, fuselage, etc.

## Slide 4: Design Choice: Push vs Pull Propeller
Pull Propeller: Higher maneuverability, lower stability
Push Propeller: Higher stability, lower maneuverability, restricts options for stabilizer positions and servo-pushrod-rudder/elevator setups. Also gets in the way of push rods.
We decided to use a pull propeller.

## Slide 5: Design Choice: Removable vs Attached Wings
Removable (Top Mounted) Wings:
  Strapped on via rubber bands attached to dowels
    Dowel supports prevent bands from damaging foam
  One continuous part
  Provides easy access to electronics in fuselage
  Reduces risk of wing damage during crash
  Center of gravity moved upward
  Can easily swap out different wing shapes
Fuselage-Attached (Fixed) Wings
  More rigid/stiff during aerobatic maneuvers which produce high wing stress
  Lowers center of gravity
  Higher risk of irreversible damage during crash
We decided to use removable, top-mounted wings

## Slide 6: Design Choice: Sensor Suite
We want (air)speed, altitude, and some sort of inertial measurement unit (IMU) for semi autonomous functions
For the IMU, only choice really a gyroscope/accelerometer board
For airspeed and altitude, two options
  Barometer (altitude) and Pitot Tube (airspeed)
    Pros: Get altitude within 0.3m, get accurate airspeed
    Cons: Two different sensors increase wiring complexity and cost, barometer needs calibration before flight
  GPS
    Pros: Can get altitude, groundspeed, position, cheaper, less complex wiring
    Cons: Get ground speed instead of airspeed (less useful for stall detection), altitude less accurate than barometer, needs to connect to GPS satellites before each flight
We chose GPS

## Slide 7: Design Choice: Landing Gear
Landing Gears:
  Take off from flat runway, get up to speed using propeller
  Let back of fuselage drag on the ground
  Landing requires a flat surface, may be more difficult
No landing gear:
  Hold plane in midair until propeller is up to speed, then toss it to take off
  Can land either by catching the plane (grabbing the fuselage), or by skidding along a flat surface
  Easier to implement
We chose not to add landing gear, for now. Should be easy to add later, if needed.

## Slide 8: Materials/Mass List
Notes: Need to get pricing from shop on transmitter/receiver pair, otherwise final. Foam mass based on solidworks.

## Slide 9: 3D Solidworks Model